Guarantee at least 3 years or 100 000 km

Car should be a model year 2017, mileage no more than 100 km.

Steering-wheel:  on the left side

Engine capacity: not less than 1.6 l- not more than 2.5 l;

Number of cylinders:   not less than 4 - not more than 6;

Power hp (horsepower): not less than 120;

Drive mechanism: full drive 4X4 or by multi-selection;

Fuel tank: not less than 40 liters;

Fuel type: petroleum/diesel;

Car gearbox:  variator or automatic gearbox not less than 6 speeds;

Fuel consumption in city: not more than 11 l;

Car length: not less than 4000 mm - not more than 4500 mm;

Car width: not less than 1700 mm - not more than 1900 mm;

Car height: not less than 1600 mm not more than 1800 mm.

Minimum requirement with regard to the car equipment

The car should be equipped with:  aluminium disks and spare tyre, as well as with all items required for changing the tire.

The car should be equipped with: the safety airbags intended at least for a driver and a passenger

The car should be equipped with:  ABS system;

The car should be equipped with:  rear visibility or parking system;

The car should be equipped with:  central lock;

The car should be equipped with: air conditioning system;

The car should be equipped with: front and rear electric windows;

The car should be equipped with: audio radio system;

The car should be equipped with: front and rear anti-fog head-lamps;

The car should be equipped with:  power-assisted steering

The cost presented by the applicant shall include all taxes prescribed by the laws of Georgia; the applicant shall also ensure registration of the car in the name of the buyer.

The car proposed shall be free from any legal and material defect.

The delivery term of the car (registration in the name of the buyer) shall be not more than 40 calendar days from execution of the Agreement. Otherwise, the amount of the penalty per each day of delay shall be 0.1% of the total cost of the car.

Untile 10 july 2017, The applicant shall submit the following information by the sealed envelope (I. Gurji 7 b) or via e-mail:

- Details of the Company;

- Information on the origin of the object of purchase;

- Price table to be filled out;

- Detailed specifications of the car proposed.

Price Table

| Name | Model | Cost in GEL | Country of Origin |
| --- | --- | --- | --- |

Upon consideration of the documentation presented, the buyer shall choose a company which will offer the best low price.

Contact person: Lasha Bokuchava, 577 61 44 44

E-mail: L.bokuchava@gipa.ge