4D Ultrasound System

Computer specs :

Windows Embedded operation system (EN language)

19’’ medical monitor(1280*1024)+10.4’’ touch monitor (minimum)

Intel i5 processor (minimum)

4G RAM (minimum)

128G SSD (minimum)

Imaging Modes :

2D, 4D, Color/PW/CW/Power/Directional Color Power Doppler,

M-Mode, Free Steering

Features :

Compound Imaging,

Speckle Reduction Imaging,

Tissue Harmonics Imaging,

4D Real-time,

Automatic Image Optimization,

Image optimization, Multi-Beam, IMT, Trapezoidal imaging

iBank database

DICOM, Ethernet, JPG/BMP/PNG,AVI, Network Storage, USB Memory Stick,

USB DVD/CD+R(W)

HDMI, 4 USB Ports, Ethernet, DICOM, Built-in speakers

Transducer Types :

Convex, Linear, Trans-vaginal, Trans-rectal, Phased array, Micro-convex, 4D Volume

Applications :

Abdominal, OB/GYN, Urology, Cardiac, Vascular, Small Parts, Pediatric, MSK

Probe Ports :

4 Active probe ports.

Cine Loop :   >10 seconds, 1200frames