Annex 1

Terms of Reference 
for the tender of Steel Works
for Darchi HPP Project, Georgia

BID-DAR-003.01-2021

AND

BID-DAR-003.02-2021

December, 2020

Contents

1.	Project Background	3

2.	Scope of Work	3

3.	Interfaces	4

4.	Appendix 1. Informational Memorandum	7

#### Project Background

Hydrolea LLC was recently acquired by Georgian Capital PLC which is a UK premium listed company investing in development and construction of hydropower projects in Georgia. Among existing power plant acquisition also included a development of greenfield project Darchi Hydroelectric Power Plant (HEPP). The project is located in the Samegrelo-Zemo Svaneti Region of Georgia near the district of Khaishi, and is owned by Hydrolea LLC though his subsidiary Darchi LLC.

The current ToR’s goal is to invite interesting, highly qualified companies to the tender for the procurement of Steel Works for the Darchi HEPP.

The current Tender consists of 2 (two) lots:

- Installation of Pipes and manufacturing, delivery and installation of the Steel Parts of the Pipeline (lot 1);

- Manufacturing, delivery, assembly and installation of Hydromechanical Mechanisms (lot 2).

Every interested company can BID for any interested lot or for both lots together.

The General Data of the hydropower project is provided in the Information Memorandum, Appendix 1 of this ToR.

#### Scope of Work

The Scope of Works under the current tender is all the work and management related to the execution of the works in all respects in accordance with the Drawings and Technical Specifications to be performed by the TENDERER including temporary works and any Variation. Works include following items but are not limited to:

Lot 1

- Installation of Steel pipes of the headrace, pressure penstock and tailrace waterways;

- Manufacturing, delivery and installation of the steel parts (angles, reducers, bifurcation, stiffeners, etc.) of the Pipeline.

Lot 2

- Manufacturing, delivery, assembly and Installation of Hydromechanical Mechanisms at the headwork structure.

#### Interfaces

Tender BID-DAR-003.01-2021 Steel Pipe Installation and Tender BID-DAR-002.01-2021 Roadworks

Pipe installation along road.:

  - Manufacture and supply by the Client

  - Putting in place by the Bidder.

  - Excavation by the Bidder.

Tender BID-DAR-003.01-2021 Steel Pipe Installation and Tender BID-DAR-002.02-2021 Road Crossings Civil works

Pipe installation when near road crossings

  - Manufacture and supply by the Client

  - Welding and connecting to the road crossing concrete block which will already have a pipe inserted to be done by the bidder.

Tender BID-DAR-003.01-2021 Steel Pipe Installation and Tender BID-DAR-003.02-2021 Headworks Civil works

Pipe installation when near Headworks

  - Manufacture and supply by the Client

  - Welding and connecting to the Headworks Pressure chamber concrete block which will already have a pipe inserted to be done by the bidder.

Tender BID-DAR-003.01-2021 Steel Pipe Installation and Tender BID-DAR-002.02-2021 Powerhouse Civil works

Pipe installation when near Powerhouse

  - Manufacture and supply by the Client

  - Welding and connecting to the Powerhouse concrete block which will already have a bifurcation inserted to be done by the bidder

Tender BID-DAR-003.01-2021 Steel Pipe Installation and Tender BID-DAR-002.02-2021 Powerhouse Civil works

Pipe installation when near Tailrace channel

  - Manufacture and supply by the Client

  - Welding and connecting to the Powerhouse Tailrace channel block which will already have a pipe inserted to be done by the bidder

Tender BID-DAR-003.01-2021Steel Pipe Installation and Tender BID-DAR-002.02-2021 Tailrace Civil works

Pipe installation when near Energy Dissipation Well channel

  - Manufacture and supply by the Client

  - Welding and connecting to the Powerhouse Tailrace channel block which will already have a pipe inserted to be done by the bidder

Tender BID-DAR-003.01-2021 Steel Pipe Installation and Tender BID-DAR-002.02-2021 Valve Chamber & Surge Chamber Civil works

Pipe installation when near Tunnel portal

  - Manufacture and supply by the Client

  - Welding and connecting to the concrete blocks which will already have a pipe inserted to be done by the bidder

Tender BID-DAR-003.01-2021 Steel Pipe Installation and Tender BID-DAR-004-2021 Tunneling Civil works

Pipe installation when near Tunnel portals

  - Manufacture and supply by the Client

  - Welding and connecting to the concrete blocks which will already have a pipe inserted to be done by the bidder

Hydromechanical works

Tender BID-DAR-003.02-2021 Hydromechanical Installation and Tender BID-DAR-002.02-2021 Headwork Civil works

Hydromechanical installation when near Headwork

  - Manufacture and supply of mechanisms/motors by the Client

  - Installation into Headwork concrete block done by the bidder

  - Concreting to be finalized by Client.

#### Appendix 1. Informational Memorandum